Iambic Electronic Keyer Utilizing The Arduino Duo
###### 1.0 Overview
This project defines an electronic keyer based on the Arduino Duo and is modeled after the Iambic Keyer described in Glen Popiel, KW5GP's book, Arduino Ham Radio[1].
[1] Popiel, Glen, KW5GP. “Arduino Ham Radio – A Radio Amateur's Guid to Open Source Electronics and Microcontroller Projects.” ARRL, 2014

REVISIONS:
03/24/2017 JRH Initial publication
###### 2.0 Requirements
###### 2.1 General Function

###### 2.2 Inputs
1. Keyer input, two lines, return to ground, with internal pullup to 5 VDC. Connector to user key using stereo audio 3.5 mm jack on front panel.
2. Power switch for internal battery
3. Toggle switch to route key input to output and bypassing the board
4. Push button #1, switch to ground
5. USB for computer or PS2 keyboard

###### 2.3 Outputs
1. Keyer output, two lines, opto isolated to radio (check specs)
2. USB connector to computer or PS2 keyboard
3. External speaker or mic output for rig interface.

###### 2.4 User Controls
1. Provide interface to keyer input of ICOM HF rigs.
2. Provide input interface to a dual paddle Iambic keyer or straight key.
3. Interface to computer USB for programming and GUI
4. Obtain power from USB (5 VDC)or an internal 9V battery with regulation to 5 VDC.

###### 2.5 Enclosure
1. Lower profile ABS plastic with no slip feet.
2. Easy access to internal battery.

###### 2.6 Functions
1. Internal speaker for CW sidetone with means to enable or disable.
2. Beacon mode to allow a CW message to key an external transmitter with variable rate, code speed, hours of operation (start stop times)
3. Provide means to implement Farnsworth Keying.
4. Provide means to vary code speed in such a way that it is easy to adjust either at high or low speed.
5. Provide means to swap dit/dah for lefties.
6. Provide means to handle a straight key, iambic paddle key, or bug.

###### 2.7 Core Components

###### 3.0 Design

Materials List
Enclosure - https://solarbotics.com/product/60105/