Iambic Electronic Keyer Utilizing The Arduino Duo
###### 1.0 Overview
This project defines an electronic keyer based on the Arduino Duo and is modeled after the Iambic Keyer described in Glen Popiel, KW5GP's book, Arduino Ham Radio[1].
[1] Popiel, Glen, KW5GP. “Arduino Ham Radio – A Radio Amateur's Guid to Open Source Electronics and Microcontroller Projects.” ARRL, 2014

###### 2.0 Requirements
###### 2.1 General Function

###### 2.2 Inputs
1. Keyer input, two lines, return to ground, with internal pullup to 5 VDC.
2. Power switch for internal battery
3. Toggle switch to route key input to output and bypassing the board
4. Push button #1, switch to ground
5. Push button #2, switch to ground

###### 2.3 Outputs
1. Keyer output, two lines, opto isolated to radio (check specs)
2. USB connector to computer

###### 2.4 User Controls
1. Connector to user key using stereo audio ⅛” jack on front panel.

1. Provide interface to keyer input of ICOM HF rigs.
2. Provide input interface to a dual paddle Iambic keyer or straight key.
3. Interface to computer USB for programming and GUI
4. Obtain power from USB (5 VDC)or an internal 9V battery with regulation to 5 VDC.

###### 2.5 Enclosure
1. Lower profile ABS plastic with no slip feet.
2. Easy access to internal battery.

###### 2.6 Functions
1. Internal speaker for CW sidetone with means to enable or disable.
2. Beacon mode to allow a CW message to key an external transmitter with variable rate, code speed, hours of operation (start stop times)
3. Provide means to vary dot/dash ratio (standard is 1:3).
4. Provide means to vary code speed in such a way that it is easy to adjust either at high or low speed.
5. Provide means to swap dit/dah for lefties.
6. Provide means to handle a straight key, iambic paddle key, or bug.

###### 2.7 Core Components

###### 3.0 Design

Materials List
Enclosure - https://solarbotics.com/product/60105/